## Slide 1: United States Coast Guard Commandant’s Marine Board of Investigation Formal Hearing, August 7-18, 2017 Seattle, Washington
Sinking of the FV DESTINATION with the loss of six lives on February 11, 2017 approximately three nautical miles north of St. George Island, Alaska
Page <number>
MBI Exhibit 001
Department of Homeland Security
United States
Coast Guard
Notes: <number>
MBI Exhibit 001
No part

## Slide 2: Conducted with the full participation of the National Transportation Safety Board
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard

## Slide 3: Casualty Overview
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: On 11 FEB 2017, at 0615 AKST, the Command Center for the Coast Guard’s District 17 received a 406 MHz EPIRB Distress Alert transmitting in the vicinity of St. George Island, Bering Sea.
CG watch standers identified the EPIRB as registered to the FV DESTINATION, and confirmed with the vessel owner that the vessel was scheduled to transit the area with 6 crew onboard.
Attempts to hail the vessel were unsuccessful. D17 launched SAR efforts, including aircraft and cutters.
By mid-day, CG aircrews and a good sam vessel a debris field in the general area of the EPIRB alert. Collected debris included the transmitting EPIRB, a life ring from the vessel, buoys, tarps and an oil sheen.
After 3 days of SAR operations, the Coast Guard suspended active searches for F/V Destination. No trace of the Life Raft or Crew were found.
SEC Anchorage initiated a preliminary marine casuality investigation, and informed CG HQ.
On 17FEB17, COMDT convened a MBI into the loss of the FV DESTINATION
No part
MBI Exhibit 001
<number>

## Slide 4: FV DESTINATION
Vessel Details | 
Official Number | 632374
Owner | F/V Destination Inc.
Flag | United States
Service | Commercial Fishing
Regulations | 46 CFR Subchapter C
Hailing Port | Sand Point, AK
Built | 1981, Brazoria, TX
Modified | 1993, Seattle, WA
Hull | Steel
Gross Tons (GRT) | 196
Length | 98.6 ft
Breadth | 32.2 ft
Depth | 13.0 ft
Propulsion | Diesel Reduction
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: The FV DESTINATION was a U.S. flag, steel hull commercial fishing vessel operated by F/V Destination Inc. The vessel was originally constructed in 1981 as an 81 foot vessel called the COMPASS ROSE, and later lengthened and widened (Sponsoned) in 1993 to its existing length of 98.6 feet.
As a Commercial Fishing Vessel, the FV DESTINATION was subject to Coast Guard regulation of 46 CFR Subchapter C – Requirements for Commercial Fishing Industry Vessels. Commercial fishing vessels are not required to be inspected by the Coast Guard for issuance of a Certificate of Inspection. However, these vessel were encouraged to voluntarily complete Coast Guard Dockside Safety Exams and receive a Safety Decal. Per the Coast Guard Authorization Act of 2010 and the Coast Guard and Maritime Transportation Act of 2012, after October 2015, Commercial Fishing Vessels operating beyond 3 nautical miles from shore are required to complete these dockside Safety Exams.
Since 1995, the FV DESTINATION held a valid Coast Guard Safety Decal, consistently completing a voluntary Dockside Safety Exam every 2 years.
No part
MBI Exhibit 001
<number>

## Slide 5: FV DESTINATION CREW
Name | Position
Jeff Hathaway | Captain
Glen Jones | Engineer/Deckhand
Ray Vincler | Deckhand
Darrik Seibold | Deckhand
Larry O’Grady | Deckhand
Kai Hamik | Deckhand
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: Crew Qualifications
  As a self-propelled, seagoing documented vessel of less than 200 gross tons, the FV DESTINATION was not required to be under the command of a Coast Guard licensed master.
No part
MBI Exhibit 001
<number>

## Slide 6: General Arrangement
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: This is a profile view of the F/V DESTINATION’s general arrangement, depicting the vessel’s three holds that can be filled with sea water to hold its catch, as well as its bait freezer, ballast tanks, cargo/gear, and fuel, lube and fresh water tanks.
No part
MBI Exhibit 001
<number>

## Slide 7: Lifesaving, Safety and Communications Equipment
Lifesaving / Safety | Communications
Personal Floatation Devices (PFD) | VHF
Immersion Suits | SSB
Life Rings | HF
Life Raft | AIS
Emergency Position Indicating Radio Beacon (EPIRB) | 
MBI Exhibit 001
<number>
* Open source web images
Department of Homeland Security
United States
Coast Guard
Notes: The FV DESTINATION was outfitted with the listed lifesaving, safety and communication equipment
No part
MBI Exhibit 001
<number>

## Slide 8: Accident Voyage (AIS Track)
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: Transit voyage: Sand Point - King Cove – Dutch Harbor - St. Paul.
In early February, the FV DESTINATION completed Cod fishing, and while in Sand Point, converted its crab pots for Opilio season.
On 08Feb at 1000, the FV Destination departed Sand Point with approximately 200 crab pots onboard.
Later that evening, the FV Destination arrived into King Cove at 7 pm. While there, the crew loaded 3,000 lbs of Sardine Bait from PeterPan Seafoods, and also completed an ADF&G Opilio Certification exam for the 200 pots onboard, the vessel departed King Cove at 10 pm enroute to Dutch Harbor.
On 09Feb at 7 pm, the FV Destination arrived into Dutch Harbor and moored at the Ku-Loss-ta-boar facility to load 7,000 lbs of Squid Bait. At 7:30, the vessel shifted births to the nearby Trident Seafoods facility, and then later departed at 11:15 enroute to St. Paul.
During the voyage up to St. Paul, it appears on two separate occasions, the FV Destination “jogged” into the seas (headed into the wind and slowed down). The first occasion was on 10Feb from 1:30 pm to 1:50pm, and the second later that same evening from 10:10-10:50.
At approximately 5:00 on 11Feb, the FV Destination cross into the western side of St. George Island.
No part
MBI Exhibit 001
<number>

## Slide 9: Departure Information: Dutch Harbor
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: This picture was taken by a crew member of a vessel moored next to the FV DESTINATION shortly after the DESTINATION moored at the Kloosterbor facility in Dutch Harbor.
No part
MBI Exhibit 001
<number>

## Slide 10: Departure Information: Dutch Harbor
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: This picture was also taken by a crew member of a vessel moored next to the FV DESTINATION shortly after the DESTINATION moored at the Kloosterbor facility in Dutch Harbor.
No part
MBI Exhibit 001
<number>

## Slide 11: Preliminary Track History Accident Voyage
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard
Notes: AIS track line of the FV Destination as it passed along the western side of St. George Is on the morning of 11 FEB..
At 0614, the FV Destination’s AIS stopped transmitting.
No part
MBI Exhibit 001
<number>

## Slide 12: Preliminary Weather Forecast Data
NWS Forecast issued for St. George/Paul Islands Thursday 09 FEB 2017
...HEAVY FREEZING SPRAY WARNING THROUGH FRIDAY NIGHT... ...SMALL CRAFT ADVISORY THROUGH FRIDAY NIGHT... .TONIGHT...NE WIND 15 KT INCREASING TO 25 KT AFTER MIDNIGHT. SEAS 7 FT. HEAVY FREEZING SPRAY. .FRI...NE WIND 30 KT. SEAS 9 FT. HEAVY FREEZING SPRAY. .FRI NIGHT...NE WIND 30 KT. SEAS 9 FT. HEAVY FREEZING SPRAY. .SAT...NE WIND 25 KT. SEAS 9 FT. .SAT NIGHT...NE WIND 20 KT. SEAS 6 FT. .SUN THROUGH TUE...N WIND 25 KT. SEAS 10 FT.
MBI Exhibit 001
<number>
Department of Homeland Security
United States
Coast Guard

## Slide 13: Preliminary Weather Data
Sunrise/ Sunset | 0955 (AKST)/ 1954 (AKST)
PAPB (land) | Winds from the NE, at 23 kts (26.4 mph), gusts of 34 kts (39 mph), light snow, Air temp of -8° C (17.6° F)
VCVA2 (marine) | Water temp -0.6° C (31° F)
Buoy 46073 (wave) | Waves from the NE 3.7 - 4.3 meters (~12 -14 ft)
MBI Exhibit Alpha
<number>
Department of Homeland Security
United States
Coast Guard
Notes: PAPB reported Winds from the NE at 23 knots with peak gusts to 34 knots, light snow, temp of -8° C, and a broken cloud ceiling at 2,000 feet agl
Closest official marine site (VCVA2) reported water temp of -0.6° C to -0.7° C.
Closest wave data site (Buoy 46073) reported waves coming fron the NE with significant wave heights between 3.7 to 4.3 meters (~12 to 14 feet)
No part
MBI Exhibit 001
<number>

## Slide 14
MBI Exhibit 001
<number>
Thank you for your attention
Department of Homeland Security
United States
Coast Guard