## Slide 1
Presented By: Robert L. Sklut
MRA Systems Engineering (contractor)
Prepared For: JTNC Standards
19 September 2022 -- revision 1.80
best to review as an MSPowerPoint Slide Show View – slides logically build for each mouse click …
Strategy Proposal for
SOSA™  SCA
Interoperability

## Slide 2: BLUF – Strategy Proposal for SOSA™  SCA Interoperability
Items shown in blue are SCA Ecosystem items, while items shown in red are SOSA™ Ecosystem items
Utilize SCA Containers as SOSA™ Ecosystem Elements, each containing a CORBA ORB and a “sufficient amount-of” the SCA Runtime (“Upper” / “Lower”) Ecosystems, allowing SCA Container contents to operate within its own SCA context
An SCA Container can function as a native SCA Ecosystem, allowing existing SCA-based Applications (e.g., WFAs, etc.), Services, and Devices to operate with minimal or no source code changes
This Ecosystem “duality” supports both SOSA™ Services and SCA Services, as-well-as SOSA™ Devices and SCA Devices
Each SCA Container includes a SOSA™ Module Agent, which makes it perform the same as a SOSA™ Module in the context of the overall SOSA™ System Management Infrastructure
Therefore, each SCA Container can also be identified as being its own unique SOSA™ Module  fulfills the SOSA™ “citizenship …” responsibilities common to all SOSA™ Modules and the SOSA™ Ecosystem Container Engine
Detailed analysis of both current and Legacy SCA-based developments have demonstrated a “mostly clean …” separation between Data_Plane and Control_Plane (“compsci-101” definitions), an advantage here:
  SCA Data_Plane messages map well – via re-marshalling tools – both in-to and out-of SOSA™ SDM (SOSA™ Data Message) structures, supporting “bulk” message data exchanges (“streams” & “packets”) between these two Ecosystems  maps well to SOSA™ Wideband Low-Latency Transport and MORA Low-Latency Bus (ML2B)
  SCA natively utilize IIOP (Internet Inter-ORB Protocol) Interaction Mechanisms, with standard IPv4 and standardized IP Ports  the generally “small” and “infrequent” SCA Control_Plane Interactions can be maintained as IIOP, using the SOSA™ Message Interconnect Transport and the VICTORY Data Bus (VDB) which is already a “general-purpose …” IPv4 physical Interconnection Mechanism
  note that it is not necessary to consider supporting IIOP on the SOSA™ Message Interconnect Transport and the VICTORY Data Bus (VDB) if the ENTIRE set of SCA Components and the SCA Ecosystem is resident to a single SOSA™ PIC
  potential SCA “special cases” involving the sequence structure CF::Properties may be handled via mappings to either (both) the SOSA™ Message Interconnect and / or the SOSA™ Wide-Band Low-Latency Interconnect
CORBA-based SCA and JTRS / JTNC API Invocation “Exceptions” will require mapping to SOSA™ -based Error Reporting and Management functions due to the “exceptionally-poor …” transposition of “Exceptions” between Ecosystems

## Slide 3
SOSA™ Module
SCA Container
2 SOSA™ 4.2 Client_COMMS & Channel_COMMS –“specialization” instances
SCA_Device
SCA_Device
SCA_Device
SCA_Device
SCA_Device
SCA_Service
SCA “Lower” Runtime
CORBA ORB
SOSA™ Module Agent
SCA Exception Handler
18
if the SCA Container is totally self-contained, then the SCA – Control_Plane never crosses SOSA™ Module boundary
if the SCA Container needs to interact with the Control_Plane functions of another SCA Container, it does so using existing IIOP (Internet Inter-ORB Protocol) IPv4 messages transported across the SOSA™ Control_Plane in native IPv4 format
SCA “Upper” Runtime
SCA Container fulfills the “citizenship” Responsibilities of a SOSA™ Module
CF::ComponentType{}
Data_Plane
(“compsci-101” definitions)
Marshall / Demarshall
CF::Properties{}
JTRS::UShortSequence{}
JTRS::OctetSequence{}
string{}
CORBA “any”
CORBA object handle
SCA_Application
SCA_Application
SCA_Application
the SCA – Data_Plane never crosses the SOSA™ Module boundary
SOSA™ Module Agent provides ALL needed mappings between the SOSA™ Module / SCA Container and the overall SOSA™ Ecosystem and Management Suite
presents a SOSA™ -conformant Module profile to the overall SOSA™ System
provides mapping between SOSA™  SCA “bulk” Data Transfers via a set of Data_Plane Marshall / Demarshall interacting with SOSA™ Data_Plane
provides mapping of SCA / CORBA Exceptions to SOSA™ Error Codes
provides needed SCA / CORBA Infrastructure and Support Components
once the SOSA™ Module / SCA Container is delivered as a reusable Base Class Entity, the SCA_Application unique element to support a COMMS Waveform
SOSA™ Module / SCA Container provides needed SCA / CORBA Infrastructure
Agent Manager

## Slide 4: SCA Container Background – 1/3
There is a “requirement …” (“desirement …”) to support the integration of Capabilities (especially, but not limited-to, existing JTRS Waveform Applications) originally developed against the SCA (Software Communications Architecture) – v2.2.2 & v4.1 – be Supported-By and Interoperable-With the SOSA™ System-of-Systems Ecosystem hosted within a CMOSS + VICTORY + MORA –based physical Solutions Architecture Implementation
WORKING PRESUMPTIONS:
utilize current SOSA™ strategy of providing hosting SOSA™ / CMOSS Chassis & Backplane of:
  availability of two Information Domains (Domain_1 = “client-side” WFA, Domain_2 = “channel-side” WFA), separated by a Cryptographic Device
  with Domain_1 utilizing SOSA™ / CMOSS resources: CP-UTP (Control Plane - Ultra-Thin Pipe) plus EP-FP (Expansion Plane - Fat Pipe)
  with Domain_2 utilizing: SOSA™ / CMOSS resources: DP-UTP (Data Plane - Ultra-Thin Pipe) plus DP-FP (Data Plane - Fat Pipe)
utilize current SOSA™ strategy of SOSA™ Message Interconnect & SOSA™ Wideband Low-Latency Interconnect logical Reference Architecture support facilities
utilize current VDB (Victory Data Bus) as a “pseudo general-purpose” IPv4 Transport in the physical CMOSS + VICTORY + MORA –based Solutions Architecture, building-upon existing VDB strategies
utilize current ML2B (MORA Low-Latency Bus) to support existing MDM (MORA Data Message) and evolving SDM (SOSA™ Data Message) Protocol and Structure definitions in the physical CMOSS + VICTORY + MORA –based Solutions Architecture, building-upon existing ML2B strategies

## Slide 5: SCA Container Background – 2/3
SCA – JTNC / JTRS WFA – JTNC / JTRS APIs:
while SCA v2.2.2 is strictly CORBA-based, and therefore utilizes GIOP (General Inter-ORB Interaction Protocol), which is IIOP (Internet Inter-ORB Protocol) in an IPv4 / IPv6 Transport Environment
while SCA v4.1 no-longer requires CORBA, the only currently supported Ecosystem is CORBA-based
while ALL of the relevant JTNC / JTRS Application, Service, and Device APIs are defined using IDL, ALL Interactions in existing JTRS Waveform Applications utilize the SCA Ecosystem as their exclusive Framework option
in-general, a “fairly-clean …” separation between Control-Plane and Data-Plane (both “comsci-101” –like definitions) Interactions exist in the JTNC / JTRS APIs and in existing JTRS Waveform Applications, with the strategy being proposed here taking advantage of this separation:
  a Control-Plane generally consisting of relatively short and infrequent Interactions (e.g., Lifecycle controls, etc.), all of which utilize the SCA Ecosystem / Framework, with most (all …) currently available legacy JTRS WFA Implementations wedded-against CORBA, even if they utilize SCA v4.1, using GIOP / IIOP
  a Data-Plane generally consisting of relatively long and frequent Interactions involving the transfer of opaque octet strings with minimal consistent & well-structured In-Band Header information between SCA Applications
while there are situations in the SCA Core Framework and JTNC / JTRS APIs which utilize the IDL type “any” – which allows for the exchange of structured data in an opaque Interaction format, and having the underlying SCA Ecosystem provide “transparent and automatic …” marshalling & demarshalling of data outside the SCA Application – its use is fairly-localized (e.g., Configuration Parameters, etc.) and can be replicated within an “SCA Adapter” to avoid needed to modify existing SCA Application software  there are well-established marshalling & demarshalling patterns that would need to be implemented in such “SCA Adapter” elements

## Slide 6: SCA Container Background – 3/3
SCA – JTNC / JTRS WFA – JTNC / JTRS APIs (continued):
the set of SCA  SOSA™ “Control-Plane” (“compsci-101” definitions) Interactions are proposed to occur without any inter-Ecosystem conversion / marshalling – demarshalling since the preferred strategy is to maintain IIOP-based communications mechanisms transported via IPv4 on the VDB
the set of SCA  SOSA™ “Data-Plane” (“compsci-101” definitions) Interactions are proposed to occur via “simple …” SCA-based Adapter Components which present the appropriate native SCA 2.2.2, SCA 4.1, JTNC-JTRS API {RSS, Application, Service, Device} Interaction Signature to the “native” SCA-based element (WFA, etc.), and providing a straightforward serialization / marshalling / demarshalling Interface Signature to the SOSA™ “Data-Plane” transport mechanisms
necessary SCA “Services” (e.g., Vocoders, File System, Timing, etc.) and “Devices” (e.g., Serial Port, PTT, etc.) are supported across the SCA Ecosystem  SOSA™ Ecosystem boundary
the principle Error-Handling strategy used in SCA 2.2.2, SCA 4.1, and the many of the JTNC / JTRS APIs is “Exception Handling”, provided via specific “Exception” definitions and their “raises” inclusions in many Invocations (verbs / calls) in their IDL-based specifications  therefore, existing JTRS WFAs and Support Applications utilize “Exceptions”, which are supported in the SCA CF (Core Framework) rather than being addressed as a Programming Language (C++) Library capability:
  while this type of “Exception Handling” strategy is well-supported in a homogeneous SCA-based CF, “Exceptions” are not currently supported in the SOSA™ CF, so SCA  SOSA™ “adapter elements” will be required to provide the necessary translation
  in-general, CF-based “Exception Handling” works well within a homogeneous CF Ecosystem, however, direct mapping of “Exceptions” between any heterogeneous CF Ecosystems is “best-avoided …”, and should NOT be incorporated into SCA CF Ecosystem  SOSA™ CF Ecosystem exchanges
  additional background regarding this Error-Handling / “Exception Handling” is included in a BACKUP section of this white paper presentation

## Slide 7: Overall System-of-Systems Context: What Counts is What’s “Inside …”
INSIDE: MRA* instances may use ANY Framework & Hardware / OS and still be a compliant SOSA™ “citizen”, with the Container providing necessary adaptation functions
OUTSIDE: SOSA™ Framework Infrastructure provides Communications Mechanisms between MRA* instances
Containers: adapt (shim) individual MRA* instances to the SOSA™ Framework Infrastructure
SOSA™ - “whatever”
Container
SOSA™ - RedHawk
Container
SOSA™ - SCA 4.1
Container
SOSA™ - SCA 2.2.2
Container
MRA* on SCA 2.2.2
MRA* on SCA 4.1
MRA* on RedHawk
MRA* on “whatever”
SOSA™ Framework Infrastructure / Communications Mechanism
Hardware / OS
Hardware / OS
Hardware / OS
SBC(s) / Single Board Computer(s)
Waveform Card(s)
etc.
* not just limited-to MRA
(Modular Radio Architecture) –
equally applicable-to ANY hosted
Application / Module / Component
If the SOSA™ Framework Infrastructure is limited to ONLY FACE™ / SOSA™ TSS Communications Mechanisms, then it is necessary for EVERY Container to translate EVERY Interaction occurring between an MRA* instance and this SOSA™ Framework Infrastructure, which will introduce unnecessary overhead whenever MRA* instances utilize the SAME Container type and need to interact across Containers  therefore, strongly-recommend an expanded use of alternative Communications Mechanisms to “share” the SOSA™ Framework Infrastructure as a “multi-lane highway”

## Slide 8: EXAMPLE #1:
8
SOSA™ Framework Infrastructure / Communications Mechanism
SCA Container
SCA Devices
SCA Runtime
SCA Container
Domain-1 WFA
SCA Runtime
SCA Container
Inter-Domain
SCA Runtime
SCA Container
Domain-2 WFA
SCA Runtime
SOSA™ Task Manager
SOSA™ System Manager
(proposed) Deployment Manager
SOSA™ Module
SOSA™ Module
yyy Container
yyy Module
yyy Runtime
RF Chain Manager
MORA
SOSA™ Device
SOSA™ Device
SOSA™
Inter-Domain
MRA implemented as a INDIVIDUAL SCA Containers for:
All co-located on single SBC or Application Card
Distributed across multiple SBCs and/or Application Cards
xxx Container
xxx Module
xxx Runtime
SCA Container
MORA Device
SCA Runtime
MRA – Any Topology
  SCA Device(s)
  SCA Domain-1 WFA
  SCA Inter-Domain
  SCA Domain-2 WFA
  MORA Device
SCA Data-Plane (“compsci-101” definition) conducted via SCA  SDM octet structure mapping performed within the SCA Containers
SCA Control-Plane (“compsci-101” definition) inter-Component interactions are POSSIBLE for SCA Control-Plane (IIOP over VDB ONLY)
All Separate SCA Containers
Distributed WFA Business Logic
Desired State: allow individual SCA Containers to interact in a “native” SCA manner across the SOSA™ Framework Infrastructure

## Slide 9: Entire “Radio” Hosted in a Single Self-Sufficient SCA Container
xxx Container
xxx Module
xxx Runtime
yyy Container
yyy Module
yyy Runtime
SCA Container
SCA Device(s)
SCA Runtime
Domain-1 WFA
Inter-Domain
Domain-2 WFA
MRA implemented as a single SCA Containers for:
  SCA Device(s)
  SCA Domain-1 WFA
  SCA Inter-Domain
  SCA Domain-2 WFA
  MORA_Device
SCA-based inter-Component interactions are POSSIBLE for BOTH the SCA Control-Plane and SCA Data-Plane
(“compsci-101” definitions)
MRA – Any Topology
Located on any single SBC
Located on any single Application Card
MORA_Device
SOSA™ Framework Infrastructure / Communications Mechanism
SOSA™ Task Manager
SOSA™ System Manager
(proposed) Deployment Manager
SOSA™ Module
SOSA™ Module
RF Chain Manager
MORA
SOSA™ Device
SOSA™ Device
SOSA™
Inter-Domain
EXAMPLE #2:
Natural State: ALL of the individual elements in the SCA Container can interact in a “native” SCA manner amongst themselves

## Slide 10: EXAMPLE #3:
SCA Container
SCA Container
Separate WFA Information Domains Hosted in Separate SCA Containers
xxx Container
xxx Module
xxx Runtime
yyy Container
yyy Module
yyy Runtime
MRA implemented as separate SCA Containers for:
MRA – Any Topology
All co-located on single SBC or Application Card
Distributed across multiple SBCs and/or Application Card
Domain-2 WFA
SCA Runtime
MORA_Device
Inter-Domain
_Device
Domain-1 WFA
SCA Runtime
SCA_Device(s)
Inter-Domain
_Device
SOSA™ Framework Infrastructure / Communications Mechanism
SOSA™ Task Manager
SOSA™ System Manager
(proposed) Deployment Manager
SOSA™ Module
SOSA™ Module
RF Chain Manager
MORA
SOSA™ Device
SOSA™ Device
SOSA™
Inter-Domain
  SCA Domain-2 WFA
  SCA Domain-1 WFA
SCA Control-Plane (“compsci-101” definition) inter-Component interactions BETWEEN Containers is POSSIBLE for SCA Control-Plane (IIOP over VDB ONLY)
SCA Data-Plane (“compsci-101” definition) inter-Component interactions BETWEEN Containers is POSSIBLE, conducted via SCA  SDM octet structure mapping performed within the SCA Containers
Note that in this Scenario, MRA utilizes the Shared Host Environment Devices and Inter-Domain Services
Desired State: allow individual SCA Containers to interact in a “native” SCA manner across the SOSA™ Framework Infrastructure

## Slide 11: WFA Implemented as a combination of a “native” SOSA™ “Client-side” Module plus SOSA™ “Channel-side” on an SCA “Card”
  SCA Domain-2 WFA
  Host Domain-1 WFA (implemented as a native SOSA™ Module)
MRA implemented across two differing Infrastructure / Ecosystems:
SCA Container
xxx Container
xxx Module
xxx Runtime
yyy Container
yyy Module
yyy Runtime
Domain-2 WFA
SCA Runtime
MRA – Any Topology
Located on any single SBC or Application Card
MORA_Device
Inter-Domain
_Device
SOSA™ / FACE™ Framework Infrastructure / Communications Mechanism
SOSA™ Task Manager
SOSA™ System Manager
(proposed) Deployment Manager
SOSA™ Module
SOSA™ Module
RF Chain Manager
MORA
SOSA™ Device
SOSA™ Device
SOSA™
Inter-Domain
EXAMPLE #4:
Note that in this Scenario, MRA utilizes the Shared Host Environment Devices and Inter-Domain Services
Note that in this Scenario, MRA Domain-1 WFA implemented as a native SOSA™ Module
Natural State: ALL of the individual elements in the SCA Container can interact in a “native” SCA manner amongst themselves

## Slide 12: inter-Container Interactions Native – Container Interactions
Operating System
Container Engine
IP Address Mapping
CPU
RAM
Disk
NIC
xxx
Container Networking Configurations:
None: Container receives a Network Stack that lacks an External Connection (stand-alone Containers and testing)
Bridge: Containers bridged by an internal Host Network, allowed to communicate with other Containers on the same Host, but cannot be accessed outside the Host
Host: Container shares the Host’s Network Namespace, granting it access to all the Host’s Network Interfaces (least complex of the External Networking Configurations, but prone to Port Conflicts)
Underlay: Host provides interfaces directly to Containers on the Host and remove the need for Port-Mapping (more efficient than Bridges)
Overlay: Networking Tunnels communicate across Hosts; Containers act like on the same Machine when they are on different Hosts
Native Application 1
Native Application 2
Control_Plane
Data_Plane
Application 1
User Space / Libraries
Container 1
Application 2
User Space / Libraries
Container 2